## Slide 1: Team JayHackers Tanvir Hossain Mahmudul Hasan Anupam Golder Zachary J Ellis Arijit Raychowdhury Tamzidul Hoque

## Slide 2
HOST IP Security Competition
4 phases of AEAD:
  Keyed INITIALIZATION
  Associated Data ABSORPTION
  Plaintext ENCRYPTION
  Keyed FINALIZATION
ASCON’s Authenticated Encryption with Associated Data (ASCON_AEAD) [ASCON21]

## Slide 3
Power Analysis
Measurement setup: ChipWhisperer toolchain, AMD/Xilinx Artix-7 FPGA-based SCA evaluation board, 10MHz CryptoCore frequency, 40MHz sampling frequency
Visible peaks during register updates  Cycle count
Parallel execution on 320-bit state + Constant-time implementation  Visually indistinguishable data-dependent leakage from single measurement
Simple Power Analysis (SPA) of INITIALIZATION Phase of ASCON_AEAD

## Slide 4
Power Analysis
INITIALIZATION phase state initialized with a 64-bit fixed and known initialization vector , a 128-bit secret key , and a 128-bit random but public nonce .
Assumption: non-repeating but attacker controllable nonce (i.e., nonce-respecting scenario).
Attack point: The first round of permutation of INITIALIZATION phase
Differential Power Analysis (DPA) Attack on INITIALIZATION Phase of ASCON_AEAD [S16]: Threat Model

## Slide 5
Power Analysis
DPA Attack on INITIALIZATION Phase of ASCON_AEAD [S16]: Selection Functions
and : secret key register bits
and : nonce register bits
: register bits
Highlighted in blue  Constant register activity
Intermediate value  2 bits from two nonce registers, 1 bit from key register
Effect of diffusion layer  Selection function to split traces based on -th bit of register update depends on 3 bits of key register and 6 bits of nonce registers and .
Total hypothesis search space: 864 for key register

## Slide 6
Power Analysis
Remaining hypothesis search space: for key register
S-box output with non-linear term  only has a result with a quadratic term containing .
and  indistinguishable due to XOR operation  Merged bit
DPA Attack on INITIALIZATION Phase of ASCON_AEAD [S16]: Selection Functions
Highlighted in blue  Constant register activity
Effect of diffusion layer  Selection function to split traces based on -th bit of register update depends on 3 bits of key register and 6 bits of nonce registers and .
Total hypothesis search space: 864 for merged key register
Recovering register:

## Slide 7
Power Analysis
Distinguisher: Difference of Means (DoM)
Number of Traces: 1M
Success rate (SR): .
DPA Attack on INITIALIZATION Phase of ASCON_AEAD [S16]: Results

## Slide 8
Power Analysis
Key idea:
  Perform multiple rounds in each cycle
  Increase hypothesis search space due to deeper diffusion of the key
Hardware overhead: Doubling of Combinational datapath
Performance: Increase in latency (due to longer critical path), Increase in throughput (due to removal of MUXing logic)
DPA Protection: Round unrolled Implementation [BSL+10,M21]

## Slide 9
Power Analysis
Key idea:
  Limit data complexity accessible to attackers
  Absorb one or few bits of nonce at a time
Proposed for Keccak (SHA-3 candidate), XOODYAK and ISAP (LWC candidates)
Hardware overhead: Lowest
Performance overhead: One-time (during INITIALIZATION)
DPA Protection: Trickled Nonce Absorption [TS14]

## Slide 10
Simple and Differential Fault Attack
A random fault injection is induced subsequent to the S-box operation in the last round of the FINALIZATION phase.
A random value was XOR’ed with the last two S-box outputs.
Due to the fault injection, the tag results changed for the golden key and nonce value.
In the next phase, we will implement Differential Fault Attack proposed in [KPW’19]
Simple Fault Attack

## Slide 11
Countermeasure for Fault Attack
Key idea:
  Generate Interleaved, Even, and Odd Parity Signatures
  Match the parity signatures with the corresponding S-box input.
Hardware overhead: Lowest
Performance overhead: Highly Accurate in terms of error detection.
Error Correction Coding based Parity Signature Generation [JMR22]
Logic Implementation of ASCON Sbox
Logic Implementation of Parity Signatures

## Slide 12
References
[W23] | Witteman M., “Security Highlight: Ascon”, 2023, URL: https://www.riscure.com/security-highlight-ascon/
[NIST23] | NIST LWC selection announcement, 2023, URL: https://csrc.nist.gov/News/2023/lightweight-cryptography-nist-selects-ascon, https://www.nist.gov/news-events/news/2023/02/nist-selects-lightweight-cryptography-algorithms-protect-small-devices
[NIST18] | NIST Call for LWC, 2018, URL: https://www.nist.gov/news-events/news/2018/04/nist-issues-first-call-lightweight-cryptography-protect-small-electronics
[Rambus23] | ASCON IP from Rambus, 2023, URL: https://www.rambus.com/blogs/rambus-ip-solution-supports-new-nist-lightweight-cryptography-algorithm/
[HN23] | HackerNews, 2023, URL: https://thehackernews.com/2023/02/nist-standardizes-ascon-cryptographic.html
[ASCON21] | ASCON final specification, URL: https://ascon.iaik.tugraz.at/specification.html , https://csrc.nist.gov/CSRC/media/Projects/lightweight-cryptography/documents/finalist-round/updated-spec-doc/ascon-spec-final.pdf
[B19] | Buchanan B., “One of the greatest advancements in Cybersecurity: The Sponge Function (Keccak, SHAKE and ASCON)”, 2019, URL: https://medium.com/asecuritysite-when-bob-met-alice/one-of-the-greatest-advancements-in-cybersecurity-the-sponge-function-keccak-and-shake-6e6c8e298682
[Keccak] | URL: https://keccak.team/
[T22] | Tezcan C., “ASCON Authenticated Encryption Scheme”, 2022, URL: https://www.youtube.com/watch?v=YIjiTB9ZxYw

## Slide 13
References
[SP21] | Steinegger, S., & Primas, R. (2021, January). A fast and compact RISC-V accelerator for ascon and friends. In Smart Card Research and Advanced Applications: 19th International Conference, CARDIS 2020, Virtual Event, November 18–19, 2020, Revised Selected Papers (pp. 53-67). Cham: Springer International Publishing. URL: https://www.youtube.com/watch?v=rC4Ib6T-qm4 , https://github.com/Steinegger/riscv_asconp_accelerator
[P22] | Primas, R., 2022, URL: https://github.com/ascon/ascon-hardware
[RD22] | Rezvani, B., Diehl W., 2022, URL: https://github.com/vtsal/ascon_lwc_aead_hash
[NGK22] | Nagpal, R., Gaj, K., Kaps, J.P., 2022, URL: https://github.com/GMUCERG/Ascon
[MGK22] | Mohajerani, K., Gaj, K., Kaps, J.P., 2022, URL: https://github.com/kammoh/bluelight/tree/api3/Ascon
[GWD+15] | Gross, H., Wenger, E., Dobraunig, C., & Ehrenhöfer, C. (2015, August). Suit up!--Made-to-Measure Hardware Implementations of ASCON. In 2015 Euromicro Conference on Digital System Design (pp. 645-652). IEEE. URL: https://github.com/IAIK/ascon_hardware/tree/master/caesar_hardware_api_v_1_0_3/ASCON_ASCON
[KKA21] | Kaur, J., Kermani, M. M., & Azarderakhsh, R. (2021). Hardware constructions for error detection in lightweight authenticated cipher ASCON benchmarked on FPGA. IEEE Transactions on Circuits and Systems II: Express Briefs, 69(4), 2276-2280.
[KHK+17] | Kumar, S., Haj-Yahya, J., Khairallah, M., Elmohr, M. A., & Chattopadhyay, A. (2017). A comprehensive performance analysis of hardware implementations of CAESAR candidates. Cryptology ePrint Archive.

## Slide 14
References
[GIB18] | Groß, H., Iusupov, R., & Bloem, R. (2018). Generic low-latency masking in hardware. IACR transactions on cryptographic hardware and embedded systems, 1-21.
[GM18] | Groß, H., & Mangard, S. (2018). A unified masking approach. Journal of cryptographic engineering, 8, 109-124.
[S16] | Samwel, N. (2016). Side-Channel Analysis of Keccak and Ascon.
[TS14] | Taha, M., & Schaumont, P. (2014, May). Side-channel countermeasure for SHA-3 at almost-zero area overhead. In 2014 IEEE International Symposium on Hardware-Oriented Security and Trust (HOST) (pp. 93-96). IEEE.
[M20] | Moos, T. (2020). Unrolled cryptography on silicon: a physical security analysis. IACR Transactions on Cryptographic Hardware and Embedded Systems, 416-442.
[BSL+10] | Bhasin, Shivam, Sylvain Guilley, Laurent Sauvage, and Jean-Luc Danger. "Unrolling cryptographic circuits: A simple countermeasure against side-channel attacks." In Topics in Cryptology-CT-RSA 2010: The Cryptographers’ Track at the RSA Conference 2010, San Francisco, CA, USA, March 1-5, 2010. Proceedings, pp. 195-207. Springer Berlin Heidelberg, 2010.
[JMR22] | J. Kaur, M. Mozaffari Kermani and R. Azarderakhsh, "Hardware Constructions for Error Detection in Lightweight Authenticated Cipher ASCON Benchmarked on FPGA," in IEEE Transactions on Circuits and Systems II: Express Briefs, vol. 69, no. 4, pp. 2276-2280, April 2022, doi: 10.1109/TCSII.2021.3136463.
[KPQ19] | K. Ramezanpour, P. Ampadu and W. Diehl, "A Statistical Fault Analysis Methodology for the Ascon Authenticated Cipher," 2019 IEEE International Symposium on Hardware Oriented Security and Trust (HOST), McLean, VA, USA, 2019, pp. 41-50, doi: 10.1109/HST.2019.8741029.